## Slide 1: PURR: A Primitive for Reconfigurable Fast Reroute
Marco Chiesa KTH Royal Institute of Technology Code: bitbucket.org/marchiesa/purr
Joint work with: Roshan Sedar Gianni Antichi Michael Borokhovich Andrzej Kamisiński Georgios Nikolaidis Stefan Schmid

## Slide 2: PURR: Thanks to my coauthors!
Joint work with: Roshan Sedar Gianni Antichi Michael Borokhovich Andrzej Kamisiński Georgios Nikolaidis Stefan Schmid

## Slide 3: Network resilience is a key yet challenging property
Image credits: route by Philipp Petzka from the Noun Project
High resilience
Why is it that hard?

## Slide 4: Routing reconvergence takes time!
Video shot taken from “Lemmings” designed and developed by DMA Design
routing restoration
failure event
control-plane detection & route recomputation
data-plane update
time

## Slide 5: Centralized controllers make reconvergence slower
Image credits: route by Philipp Petzka from the Noun Project
Advanced SDN routing e.g., intent-based logically centralized SDN
failure occurs
control-plane detection & route recomputation
data-plane update
time
High resilience

## Slide 6: Hard to recover within 50ms!
[1] On low-latency-capable topologies, and their impact on the design of intra-domain routing. In SIGCOMM 2018
Image credits: route by Philipp Petzka from the Noun Project
Advanced SDN routing e.g., intent-based logically centralized SDN
High resilience
“[carrier-grade networks] level of availability requires substantial over-provisioning and fast reroute local recovery, e.g., within 50 milliseconds“ [1]
failure occurs
control-plane detection & route recomputation
data-plane update
time

## Slide 7: Fast Reroute (FRR): pre-computing failover paths
B
C
A
primary
2nd backup
backup
match/actions (e.g., at X)
FRR entails solving two orthogonal problems:
control-plane: compute network-wide primary/backup forwarding rules
control plane
FRR actions (e.g., at X)
1
FRR1 >> fwd A
X
dst = A >> FRR1
B
C

## Slide 8: Fast Reroute (FRR): pre-computing failover paths
B
C
A
primary
2nd backup
backup
match/actions (e.g., at X)
FRR entails solving two orthogonal problems:
control-plane: compute network-wide primary/backup forwarding rules
control plane
FRR actions (e.g., at X)
1
FRR1 >> fwd A
FRR2 >> fwd B C A
X
dst = A >> FRR1
dst = B >> FRR2
B
C

## Slide 9: Fast Reroute (FRR): pre-computing failover paths
2
match/actions (e.g., at X)
FRR entails solving two orthogonal problems:
control-plane: compute network-wide primary/backup forwarding rules
data-plane: support conditional forwarding in each switch
control plane
FRR actions (e.g., at X)
1
B
C
A
primary
2nd backup
backup
X
header/metadata
parser
deparser
packet pipeline
FRR1 >> fwd A B C
FRR2 >> fwd C B A
dst = A >> FRR1
dst = B >> FRR2
dst = A >> FRR1
dst = B >> FRR2
FRR1 >> fwd A B C
FRR2 >> fwd C B A

## Slide 10: The goal of this talk: implement a FRR primitive that minimizes pipeline resource consumption
Output
Input
2
FRR actions (e.g., at X)
FRR1 >> fwd A B C
FRR2 >> fwd C B A
header/metadata
parser
deparser
dst = A >> FRR1 dst = B >> FRR2
FRR1 >> fwd A B C FRR2 >> fwd C B A
packet pipeline
PURR: A building block for implementing arbitrary FRR mechanisms
Cat by dDara from the Noun Project

## Slide 11: PURR applies to P4 programmable switches
Advanced SDN routing (e.g., intent-based logically centralized SDN)
High availability
(e.g., within 50 milliseconds”[1])
[1] On low-latency-capable topologies, and their impact on the design of intra-domain routing. In SIGCOMM 2018
High flexibility
(e.g., reconfigurable P4 dataplanes)
Image credits: route by Philipp Petzka from the Noun Project
Packets in
Input headers & metadata
Packets out
Packet recirculation
stage 1
stage …
stage N
ingress buffer
Parser
Runtime P4 (Control plane)
simplified pipeline
Resources:
- SRAM (exact matches), e.g., 2M entries
- TCAM (wildcard matches), e.g., 100K entries
- ALU

## Slide 12: PURR applies to P4 programmable switches
Advanced SDN routing (e.g., intent-based logically centralized SDN)
High availability
(e.g., within 50 milliseconds”[1])
[1] On low-latency-capable topologies, and their impact on the design of intra-domain routing. In SIGCOMM 2018
High flexibility
(e.g., reconfigurable P4 dataplanes)
Image credits: route by Philipp Petzka from the Noun Project
Packets in
Input headers & metadata
Packets out
Packet recirculation
stage 1
stage …
stage N
ingress buffer
Parser
Runtime P4 (Control plane)
simplified pipeline
Resources:
- SRAM (exact matches), e.g., 2M entries
- TCAM (wildcard matches), e.g., 100K entries
- ALU
How do we realize FRR in P4?
No P4 built-in FRR primitive but… a programmable pipeline: many approaches are possible!

## Slide 13: First approach: packet recirculation
match tag | action | 
 | fwd | write & recirculate
1 | 1 | tag := 2
2 | 2 | tag := 3
3 | 3 | tag := 4
4 | 4 | -
FRR1 = 1 2 3 4
port 1 fails
port 2 fails
Input
throughput reduction
latency increase

## Slide 14: FRR recirculation has high memory occupancy
throughput reduction
latency increase
match tag | action | 
 | fwd | write & recirculate
1 | 1 | tag := 2
2 | 2 | tag := 3
3 | 3 | tag := 4
4 | 4 | -
5 | 4 | tag:= 6
6 | 3 | tag = 7
7 | 2 | tag = 8
8 | 1 | -
port 4 fails
port 3 fails
FRR1 = 1 2 3 4
FRR2 = 4 3 2 1
Input
throughput reduction
latency increase
high memory overhead

## Slide 15: PURR: a primitive for reconfigurable FRR
A building block for implementing arbitrary FRR mechanisms
parallel search with TCAM
model port status -> flip one single bit
Cat by dDara from the Noun Project
high throughput | low forwarding latency | efficient reroute | flexibility | small forwarding tables
support arbitrary FRR mechanisms, i.e., arbitrary FRR input sequences

## Slide 16: PURR: a primitive for reconfigurable FRR
A building block for implementing arbitrary FRR mechanisms
intriguing connection to (algorithmic) “string theory”
Cat by dDara from the Noun Project
high throughput | low forwarding latency | efficient reroute | flexibility | small forwarding tables

## Slide 17: PURR: Encoding FRR in the packet metadata
Input
FRR1 = 1 2 3 4
packet metadata
FRR = 1
port status
1 1 1 1
P4 register
port status
1 1 1 1
port 1 is active
port 2 is active
match | action
port status | fwd
1 * * * | 1
* 1 * * | 2
* * 1 * | 3
* * * 1 | 4
TCAM wildcard match memory

## Slide 18: PURR: Encoding FRR in the packet metadata
Input
match | action
port status | fwd
1 * * * | 1
* 1 * * | 2
* * 1 * | 3
* * * 1 | 4
FRR1 = 1 2 3 4
port status
1 1 1 1
packet metadata
FRR = 1
TCAM wildcard match memory

## Slide 19: PURR: Encoding FRR in the packet metadata
Input
match | action
port status | fwd
1 * * * | 1
* 1 * * | 2
* * 1 * | 3
* * * 1 | 4
FRR1 = 1 2 3 4
port status
0 1 1 1
packet metadata
FRR = 1
port 1 fails
TCAM wildcard match memory

## Slide 20: PURR: Encoding FRR in the packet metadata
Input
match | action
port status | fwd
1 * * * | 1
* 1 * * | 2
* * 1 * | 3
* * * 1 | 4
port 2 fails
FRR1 = 1 2 3 4
port status
0 0 1 1
packet metadata
FRR = 1
TCAM wildcard match memory

## Slide 21: PURR: One tempting option: “Duplication” TCAM
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1
match |  | action
FRR | port status | fwd
1 | 1 * * * | 1
1 | * 1 * * | 2
1 | * * 1 * | 3
1 | * * * 1 | 4
2 | * 1 * * | 2
2 | * * 1 * | 3
2 | * * * 1 | 4
2 | 1 * * * | 1
similar to FRR recirculation:
high memory overhead
port status
0 0 1 1
packet metadata
FRR = 2

## Slide 22: PURR: Encoding FRR in the packet metadata
match | action write
 | frr_ports
FRR = 1 | 1 1 1 1 0
FRR = 2 | 0 1 1 1 1
match | action write
 | frr_ports
FRR = 1 | b1b2b3b4b5
FRR = 2 | 0 1 1 1 1 0 0
FRR = 3 | 0 0 1 1 1 1 0
FRR = 4 | 0 0 0 1 1 1 1
bit-to-port mapping
1 2 3 4 1
Encoding FRR input:
add a packet metadata field frr_ports
map bits to the switch ports
set bit to 1 to include a port
set bit to 0 to skip a port
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1
port status
1 1 1 1
packet metadata
FRR = 1

## Slide 23: PURR: Encoding FRR in the packet metadata
match | action write
 | frr_ports
FRR = 1 | 1 1 1 1 0
FRR = 2 | 0 1 1 1 1
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1
port status
1 1 1 1
packet metadata
FRR = 1
bit-to-port mapping
1 2 3 4 1
match |  | action
frr_ports | port status | fwd
1 * * * * | 1 * * * | 1
* 1 * * * | * 1 * * | 2
* * 1 * * | * * 1 * | 3
* * * 1 * | * * * 1 | 4
* * * * 1 | 1 * * * | 1

## Slide 24: PURR: Encoding FRR in the packet metadata
match | action write
 | frr_ports
FRR = 1 | 1 1 1 1 0
FRR = 2 | 0 1 1 1 1
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1
port status
1 1 1 1
packet metadata
FRR = 1
bit-to-port mapping
1 2 3 4 1
match |  | action
frr_ports | port status | fwd
1 * * * * | 1 * * * | 1
* 1 * * * | * 1 * * | 2
* * 1 * * | * * 1 * | 3
* * * 1 * | * * * 1 | 4
* * * * 1 | 1 * * * | 1

## Slide 25: PURR: Encoding FRR in the packet metadata
match | action write
 | frr_ports
FRR = 1 | 1 1 1 1 0
FRR = 2 | 0 1 1 1 1
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1
port status
0 1 1 1
packet metadata
FRR = 1
bit-to-port mapping
1 2 3 4 1
match |  | action
frr_ports | port status | fwd
1 * * * * | 1 * * * | 1
* 1 * * * | * 1 * * | 2
* * 1 * * | * * 1 * | 3
* * * 1 * | * * * 1 | 4
* * * * 1 | 1 * * * | 1

## Slide 26: PURR: re-cycling TCAM entries
match | action write
 | frr_ports
FRR = 1 | 1 1 1 1 0
FRR = 2 | 0 1 1 1 1
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1
port status
1 1 1 1
packet metadata
FRR = 2
bit-to-port mapping
1 2 3 4 1
match |  | action
frr_ports | port status | fwd
1 * * * * | 1 * * * | 1
* 1 * * * | * 1 * * | 2
* * 1 * * | * * 1 * | 3
* * * 1 * | * * * 1 | 4
* * * * 1 | 1 * * * | 1

## Slide 27: The key problem: How to compute the bit-to-port mapping that minimizes memory occupancy?
bit-to-port mapping = .2 3 1 0 2 1 3
FRR1 = 2 3 1 0
FRR2 = 0 2 1 3
FRR3 = 3 0 2 1
FRR4 = 1 0 2 3
FRR1 = 2 3 1 0 FRR2 = 0 2 1 3 FRR3 = 3 0 2 1 FRR4 = 1 0 2 3
Shortest Common Supersequence (SCS) problem without repetitions
SCS without repetitions is computationally hard (based on [2])
Dynamic Programming (DPSCS) computes optimum in exponential time
bit-to-port mapping = ?
[2 ]T. Jiang, M. Li. On the approximation of shortest common supersequences and longest common subsequences. In Journal on Computing.

## Slide 28: Fast-Greedy: a heuristic for solving this specific SCS
idea: remove the most frequent left-most element among the longest sequences
See the paper for:
multi-table optimization
F1=2 3 1 0
F2=2 0 1 3
F3=2 3 0 1
F4=3 1 2 0
remove 2
F1=3 1 0
F2=0 1 3
F3=3 0 1
F4=3 1 2 0
remove 3
F1=1 0
F2=0 1 3
F3=0 1
F4=1 2 0
remove 0
F1=1 0
F2=1 3
F3=1
F4=1 2 0
remove 1
F1=0
F2=3
F3= ---
F4=2 0
remove 2
F1=0
F2=3
F3= ---
F4=0
remove 0
F1= ---
F2=3
F3= ---
F4= ---
remove 3
SCS =
2
3
0 1 2 0 3

## Slide 29: Implementation feasibility
P4-based implementations:
implemented different FRR mechanisms in P4 using PURR (e.g., F10 [1], arborescences [2], BFS, DFS, rotor router [3])
compiled on Tofino
FPGA-based implementation:
implemented PURR on the NetFPGA-SUME platform
[1] V. Liu et al. "F10: A Fault-Tolerant Engineered Network" in NSDI 2013
[2] M. Chiesa et al. "On the Resiliency of Randomized Routing Against Multiple Edge Failures" in Transactions on Networking 2016
[3] Borokhovich et al ””Graph exploration algorithms” in HotSDN 2013

## Slide 30: Evaluation: How does the FRR implementation impact memory and performance?
Two subquestions:
How much memory does PURR save?
How does performance in a datacenter vary depending on how one implements a FRR primitive?
See the paper for:
multi-table optimization
random vs tree-based FRR sequences
FPGA chip occupancy
low-size FRR sequences

## Slide 31: How much memory does PURR save? The “circular sequences” case
Input:
switch with k ports
10 circular set of FRR sequences
“Duplication TCAM” FRR:
k2 number of TCAM entries
With PURR encoding:
k-1 number of TCAM entries
10 Top-of-Rack switches in a datacenter with F10 FRR [nsdi-13]
10 destinations with the "k arc-disjoint" FRR mechanism [ton-16]
[nsdi-13] V. Liu et al. "F10: A Fault-Tolerant Engineered Network" in NSDI 2013
[ton-16] M. Chiesa et al. "On the Resiliency of Randomized Routing Against Multiple Edge Failures" in Transactions on Networking 2016

## Slide 32: How much memory does PURR save? The “circular sequences” case
Input:
switch with k ports
10 circular set of FRR sequences
“Duplication TCAM” FRR:
k2 number of TCAM entries
With PURR encoding:
k-1 number of TCAM entries
For k = 24
92% less TCAM entries
470 instead of 5.760
For k = 48
96% less TCAM entries
950 instead of 23.040
[nsdi-13] V. Liu et al. "F10: A Fault-Tolerant Engineered Network" in NSDI 2013
[ton-16] M. Chiesa et al. "On the Resiliency of Randomized Routing Against Multiple Edge Failures" in Transactions on Networking 2016

## Slide 33: How much memory does PURR save? Fast-greedy performs close to the optimum
avg. #TCAM entries
number of FRR sequences
30
20
10
0
8
2
3
4
5
6
7
Input: randomly generated set of FRR sequences of length 7
number of FRR sequences
2
3
4
5
6
7
106105
104
103
102
101
10010-1
avg. time [ms]
DPSCS
Fast-greedy
Fast-greedy
DPSCS

## Slide 34: How much memory does PURR save? Fast-greedy scales to large number of sequences
avg. TCAM bits
Input: randomly generated set of FRR sequences
sequence size=32
sequence size=16
sequence size=8
sequence size=32
sequence size=16
sequence size=8
32 factorial possible FRR sequences The “duplication” TCAM or recirculation FRR approaches would not scale
avg. #TCAM entries

## Slide 35: How does FCT vary depending on the FRR primitive? PURR improves both FCT and throughput
Throughput [Gbps]
Load [%]
101
100
10
20
30
40
50
60
70
FRR recirculation
immediate reconvergence
2.7x
Small flows FCT [ms]
Load [%]
2.0
1.5
1.0
0.5
0.0
10
20
30
40
50
60
70
FRR recirculation
immediate reconvergence
2.4x
NS-3 simulations
Topology: 32-server Clos network, 10Gbps links
Workload: data-mining Transport: DCTCP One link failure at 0.5s

## Slide 36: How does FCT vary depending on the FRR primitive? PURR improves both FCT and throughput
Throughput [Gbps]
Load [%]
101
100
10
20
30
40
50
60
70
FRR recirculation
immediate reconvergence
Small flows FCT [ms]
Load [%]
2.0
1.5
1.0
0.5
0.0
10
20
30
40
50
60
70
FRR recirculation
immediate reconvergence
1.4x
NS-3 simulations
Topology: 32-server Clos network, 10Gbps links
Workload: data-mining Transport: DCTCP One link failure at 0.5s
purr
purr
2x

## Slide 37: Conclusions: Keep calm and enjoy programmability
Fast Reroute is a critical functionality in today’s network
requires high throughput, low latency, fast reactiveness, small forwarding tables
P4 does not define an FRR built-in primitive
pipeline compilers and control-plane must program the P4 pipeline
PURR: We propose a lightweight TCAM-based FRR primitive
an intriguing connection to algorithmic string theory
no FRR-tailored hardware support
improve performance by a factor of 2x w.r.t. FRR recirculation
Marco Chiesa KTH Royal Institute of Technology Code: bitbucket.org/marchiesa/purr
Thank you!
Cat by dDara from the Noun Project
reusable

## Slide 38: Backup slides

## Slide 39: Smaller sequences on switches with high-density ports
Input:
a 64-port programmable switch
all possible three ports FRR sequences
“Duplication TCAM” approach:
#TCAM entries = 64*63*62*3 = 750K
TCAM memory = 750K * (20 + 3) = 17.2Mb
PURR encoding approach:
#TCAM entries < (64*3) = 192
TCAM memory < 192 * (64*4) = 50Kb
more than 99% memory reduction!
FRR recirculation:
#TCAM entries = 64*63*62 = 250K
TCAM memory = 250K * (17+3) = 5Mb

## Slide 40: Three naïve approaches to implementing FRR
low
low
low
high
high
high
low
low
high
high
high
high
high
high
high
FRR recirculation
FRR sequential
FRR parallel duplication
throughput
latency
reactiveness
memory
flexibility

## Slide 41: Second approach: sequential search
match | action
FRR = 1 | fwd(1)
match | action
FRR = 1 | fwd(2)
match | action
FRR = 1 | fwd(3)
match | action
FRR = 1 | fwd(4)
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1 FRR3 = 3 4 1 2 FRR4 = 4 1 2 3

## Slide 42: Second approach: sequential search
match | action
FRR = 1 | fwd(1)
FRR = 2 | fwd(2)
match | action
FRR = 1 | fwd(2)
FRR = 2 | fwd(3)
match | action
FRR = 1 | fwd(3)
FRR = 2 | fwd(4)
match | action
FRR = 1 | fwd(4)
FRR = 2 | fwd(1)
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1 FRR3 = 3 4 1 2 FRR4 = 4 1 2 3

## Slide 43: Second approach: sequential search
match | action
FRR = 1 | fwd(1)
FRR = 2 | fwd(2)
FRR = 3 | fwd(3)
match | action
FRR = 1 | fwd(2)
FRR = 2 | fwd(3)
FRR = 3 | fwd(4)
match | action
FRR = 1 | fwd(3)
FRR = 2 | fwd(4)
FRR = 3 | fwd(1)
match | action
FRR = 1 | fwd(4)
FRR = 2 | fwd(1)
FRR = 3 | fwd(2)
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1 FRR3 = 3 4 1 2 FRR4 = 4 1 2 3

## Slide 44: Second approach: sequential search
match | action
FRR = 1 | fwd(1)
FRR = 2 | fwd(2)
FRR = 3 | fwd(3)
FRR = 4 | fwd(4)
match | action
FRR = 1 | fwd(2)
FRR = 2 | fwd(3)
FRR = 3 | fwd(4)
FRR = 4 | fwd(1)
match | action
FRR = 1 | fwd(3)
FRR = 2 | fwd(4)
FRR = 3 | fwd(1)
FRR = 4 | fwd(2)
match | action
FRR = 1 | fwd(4)
FRR = 2 | fwd(1)
FRR = 3 | fwd(2)
FRR = 4 | fwd(3)
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1 FRR3 = 3 4 1 2 FRR4 = 4 1 2 3

## Slide 45: A sequential search wastes hardware resources
match | action
FRR = 1 | fwd(1)
FRR = 2 | fwd(2)
FRR = 3 | fwd(3)
FRR = 4 | fwd(4)
match | action
FRR = 1 | fwd(2)
FRR = 2 | fwd(3)
FRR = 3 | fwd(4)
FRR = 4 | fwd(1)
match | action
FRR = 1 | fwd(3)
FRR = 2 | fwd(4)
FRR = 3 | fwd(1)
FRR = 4 | fwd(2)
match | action
FRR = 1 | fwd(4)
FRR = 2 | fwd(1)
FRR = 3 | fwd(2)
FRR = 4 | fwd(3)
Input
FRR1 = 1 2 3 4 FRR2 = 2 3 4 1 FRR3 = 3 4 1 2 FRR4 = 4 1 2 3
increased latency
waste of resources at each stage
many updates to the forwarding table
port 2 fails
port 3 fails

## Slide 46: PURR improves both FCT and throughput Two link failures, higher gains
NS-3 simulations
Topology: 32-server Clos network, 10Gbps links, 10 link latency
Workload: data-mining Transport: DCTCP
1.7x
1.8x

## Slide 47: Evaluation: Random vs tree-based sequences

## Slide 48: The web search workload
NS-3 simulations
Topology: 32-server Clos network, 10Gbps links, 10 link latency
Workload: web-search Transport: DCTCP