## Slide 1
Ehsan Tohidi, Max Franke, André Drummond,
Stefan Schmid, Admela Jukan, and Slawomir Stańczak
RIS-Assisted 6G Networks: Challenges and Tradeoffs in Control Standardization

## Slide 2
Ehsan Tohidi, Max Franke, André Drummond,
Stefan Schmid, Admela Jukan, and Slawomir Stańczak
RIS-Assisted 6G Networks: Challenges and Tradeoffs in Control Standardization
Much research on RIS devices and physical properties, network-level studies rare. We need models for understanding performance and standards. What is unique here? And implications for control plane?

## Slide 3: Campus Networks (e.g., Smart Factories)
Reliability Issue
E. Tohidi et al., "Reliability Assurance in RIS-Assisted 6G Campus Networks,"
20th International Conference on the Design of Reliable Communication Networks (DRCN), 2024.

## Slide 4: Campus Networks (e.g., Smart Factories)
Reliability Issue
E. Tohidi et al., "Reliability Assurance in RIS-Assisted 6G Campus Networks,"
20th International Conference on the Design of Reliable Communication Networks (DRCN), 2024.
LoS blocking especially critical for mmWave and sub-THz!

## Slide 5: Campus Networks (e.g., Smart Factories)
Reliability Assurance: RIS
E. Tohidi et al., "Reliability Assurance in RIS-Assisted 6G Campus Networks,"
20th International Conference on the Design of Reliable Communication Networks (DRCN), 2024.

## Slide 6: Introduction

## Slide 7: Introduction
What is a Reconfigurable Intelligent Surface?
Reconfigurable Intelligent Surface (RIS) is a planar surface comprising a large number of passive reflecting elements, each of which is able to induce a controllable phase change to the incident signal independently
Specular reflection to anomalous reflection
Advantages
Anomalous reflection - Reconfigurability
Disadvantage
Multiplicative fading due to cascaded channel
E. Tohidi et al., "Reliability Assurance in RIS-Assisted 6G Campus Networks,"
20th International Conference on the Design of Reliable Communication Networks (DRCN), 2024.

## Slide 8: Introduction
What is a Reconfigurable Intelligent Surface?
Reconfigurable Intelligent Surface (RIS) is a planar surface comprising a large number of passive reflecting elements, each of which is able to induce a controllable phase change to the incident signal independently
Specular reflection to anomalous reflection
Advantages
Anomalous reflection - Reconfigurability
Disadvantage
Multiplicative fading due to cascaded channel
E. Tohidi et al., "Reliability Assurance in RIS-Assisted 6G Campus Networks,"
20th International Conference on the Design of Reliable Communication Networks (DRCN), 2024.
Aka „double path loss“

## Slide 9: Key Technology for 6G?
1G-4G Sector antenna
Fixed radiation pattern
Fortunate user
Unfortunate user
5G: Adaptive multi-user beamforming
6G: Control objects in the environment?
?
credit: Emil Björnson

## Slide 10: Key Technology for 6G?
Wall penetration: dB or more
Reflection
Base station
credit: Emil Björnson

## Slide 11: System Model
RIS-assisted wireless communication system
  BS, multiple RISs, and several UEs
BS and RISs are static, while UEs can be static or mobile
Even BS-UE initial access may take time: requires alignment of directional antennas both at BS and UE (using beam sweeping, fixed codebooks).

## Slide 12: RIS-ASSISTED LINK CHARACTERISTICS

## Slide 13: Cascaded Channel
Additional path loss
RIS-assisted link, consists of two concatenated links—commonly referred to as a cascade channel—namely the BS-RIS and RIS-UE links
This inherent characteristic of RIS-assisted systems results in lower overall channel gains than direct links.
Another key factor affecting the RIS-assisted channel gain is the RIS gain
  The RIS ability to capture incident signal energy and redirect it toward the intended receiver
  larger RIS surfaces yield higher RIS gain and, consequently, higher RIS-assisted channel gain.

## Slide 14: Cascaded Channel
Additional path loss
RIS-assisted link, consists of two concatenated links—commonly referred to as a cascade channel—namely the BS-RIS and RIS-UE links
This inherent characteristic of RIS-assisted systems results in lower overall channel gains than direct links.
Another key factor affecting the RIS-assisted channel gain is the RIS gain
  The RIS ability to capture incident signal energy and redirect it toward the intended receiver
  larger RIS surfaces yield higher RIS gain and, consequently, higher RIS-assisted channel gain.
Other factors matter, e.g., when located in near-field. Our focus here however far-field (each RIS serves one UE at a time).

## Slide 15: Reconfiguration Time
Critical and Non-negligible
RIS can perform beamforming by dynamically altering the phases of the reflected waves.
Various technologies, each with its cost, energy consumption, and response time characteristics
  Varactor diodes and PIN diodes, can achieve reconfiguration times in the range of a few nanoseconds
  Liquid crystals (LC), have reconfiguration times that can extend beyond ten milliseconds
LC technology offers advantages such as cost-effectiveness, scalability, low energy consumption, and the ability to provide continuous phase shifting.
  Relatively longer reconfiguration time associated with LC highlights the importance of carefully considering this factor in practical deployments.

## Slide 16: Beam Leap While Tracking
Sudden shift in the required beam direction
In a mobile UE scenario, due to the movement of the UE, the device currently served via a RIS-assisted link may enter a blind spot of the RIS
  BS may be able to serve the UE directly if the direct linkis no longer blocked at the new location
  the system may need to switch to another RIS that can provide coverage in the UE’s new location
the next beam selected by the BS will likely be significantly different from the current one, as it may need to point in a completely different direction
  Starkly contrasts conventional tracking methods, where beam sweeping typically occurs within neighboring beams to account for small movements of the UE.

## Slide 17: Beam Leap While Tracking
Sudden shift in the required beam direction
In a mobile UE scenario, due to the movement of the UE, the device currently served via a RIS-assisted link may enter a blind spot of the RIS
  BS may be able to serve the UE directly if the direct linkis no longer blocked at the new location
  the system may need to switch to another RIS that can provide coverage in the UE’s new location
the next beam selected by the BS will likely be significantly different from the current one, as it may need to point in a completely different direction
  Starkly contrasts conventional tracking methods, where beam sweeping typically occurs within neighboring beams to account for small movements of the UE.
Another new aspect! Requires beam jump/leap procedure.

## Slide 18: CONTROL PLANE ASPECTS: Use Cases

## Slide 19: Scenarios and Challenges for Control Plane
Depending on Use Case

## Slide 20: CONTROL PLANE ASPECTS: Proposed RIS Control

## Slide 21: Proposed RIS Control
RIS-assisted Link Restoration Procedure
Link restoration: establishing a RIS-assisted link for a UE that was initially connected directly to the BS. Triggered based on:
  Predicted (“anticipated”) based on prior information available to the BS (e.g., radio maps of the environment).
  Continuously monitor channel quality and detect link degradation trends.
BS triggers the network controller initiate the link restoration
Network controller creates a pool of candidate RISs
  Resource allocation algorithm to select the RIS
The BS and the RIS controller are informed and configured accordingly
BS’s perspective: the shift in beam direction—from the direct link toward the UE to the beam aimed at the RIS, i.e., “beam leap”.

## Slide 22: Proposed RIS Control
RIS-assisted Link Restoration Procedure
Link restoration: establishing a RIS-assisted link for a UE that was initially connected directly to the BS. Triggered based on:
  Predicted (“anticipated”) based on prior information available to the BS (e.g., radio maps of the environment).
  Continuously monitor channel quality and detect link degradation trends.
BS triggers the network controller initiate the link restoration
Network controller creates a pool of candidate RISs
  Resource allocation algorithm to select the RIS
The BS and the RIS controller are informed and configured accordingly
BS’s perspective: the shift in beam direction—from the direct link toward the UE to the beam aimed at the RIS, i.e., “beam leap”.
Triggered by the BS.
Could also require handover (new BS): not considered here.
Depending on demand, available resources, priority…
Accuracy depends on time elapsed since last connection, mobility speed, etc.

## Slide 23: Proposed RIS Control
Beam-Tracking in RIS-assisted Link
Connection quality degradation
RIS controller is notified to adjust the beam
  Localized beam sweeping through a few neighboring beams
  Narrow beams of RIS more neighboring beams (compared to conventional beam sweeping)
BS keeps its beam locked in the optimal direction toward the RIS
  No beam sweeping at the BS

## Slide 24: Proposed RIS Control
Beam-Tracking in RIS-assisted Link
Connection quality degradation
RIS controller is notified to adjust the beam
  Localized beam sweeping through a few neighboring beams
  Narrow beams of RIS more neighboring beams (compared to conventional beam sweeping)
BS keeps its beam locked in the optimal direction toward the RIS
  No beam sweeping at the BS
RIS: localized sweep compared to BS!
BS can lock beam: same RIS.
Due to larger surface, RIS beams are narrower than BS‘ beams.

## Slide 25: Proposed RIS Control
Try BS-Direct link
BS will attempt to re-establish a direct link whenever possible
  transition from the RIS-assisted link to a direct BS-UE
This direction is less critical than restoration: improves quality.

## Slide 26: Proposed RIS Control
Keep Connection during Intermittent LoS Connection
Frequent changes in connection status—between LoS and non-line-of-sight (nLoS)—within short time intervals complicate transitions.
This rapid fluctuation in connection quality can lead to connection loss, as the link may not be re-established within the limited available time.
Proposed solution: maintain the previous connection for a short duration until the new connection is established.

## Slide 27: Proposed RIS Control
Link Backup – Multi connectivity
Abrupt channel behavior in high frequency, e.g., terahertz
Link backup strategy
  Candidate RIS reserved for potential abrupt disconnections
  The problem of over allocation (not scalable)
Multiconnectivity
  Provide multiple links simultaneously
  Seamless switch to the new link
Price: requires more resources!

## Slide 28: RIS-ASSISTED 6G NETWORKS

## Slide 29: RIS-ASSISTED 6G NETWORKS
RIS in Practice
Simplified model (optimistic): max speed an UE can move is limited by reconfiguration time and #UEs
RIS reconfiguration time assumed to be 10 ms
5G and beyond standards in handover interruption time

## Slide 30: RIS-ASSISTED 6G NETWORKS
RIS in Practice
Simplified model (optimistic): max speed an UE can move is limited by reconfiguration time and #UEs
RIS reconfiguration time assumed to be 10 ms
5G and beyond standards in handover interruption time
Typical values for indoor. For outdoor, less well suited?
Delay due to switching between users.

## Slide 31: Summary
RIS promising but not much literature on link level studies yet
Reality is complex: call to community to conduct more research on realistic models and prototypes
A prerequisite for standardization

## Slide 32: Thank you! Questions?