## Slide 1
  “We cannot direct the wind,
  but we can adjust the sails.”
  (Folklore)
Self-Adjusting Networks
Stefan Schmid
Acknowledgements:

## Slide 2: Trend Data-Centric Applications
1
Datacenters (“hyper-scale”)
Traffic
Growth
Source: Facebook
Interconnecting networks: a critical infrastructure of our digital society.
+network
Notes: The interconnecting networks have become a critical infrastructure of our digital society.

## Slide 3: The Problem Huge Infrastructure, Inefficient Use
⇢ Network equipment reaching
capacity limits
⇀ Transistor density rates stalling
⇀ “End of Moore‘s Law in networking” [1]
⇢ Hence: more equipment,
larger networks
⇢ Resource intensive and:
inefficient
Annoying for companies,
opportunity for researchers
[1] Source: Microsoft, 2019
Gbps/€
Time
Notes: This may be annoying for companies, it introduces a great opportunity for researchers.

## Slide 4: Root Cause Fixed and Demand-Oblivious Topology
3
How to interconnect?
Notes: A route cause for this inefficiency is related to how we interconnect these distributed systems.

## Slide 5: Root Cause Fixed and Demand-Oblivious Topology
Many flavors,
but in common: fixed and oblivious to actual demand.
3
Notes: Today, many different network toplogies are used in datacenters, such as this one.
However, they all have in common that they are fixed and oblivious to the actual demand.

## Slide 6: Root Cause Fixed and Demand-Oblivious Topology
Highway which ignores actual traffic: frustrating!
Many flavors,
but in common: fixed and oblivious to actual demand.
3
Notes: You can think of it like a highway which ignores the actual traffic: it can be frustrating.
Here it would be much better if the other lanes could be used as well. And maybe in the evening the other way round.

## Slide 7: Our Vision Flexible and Demand-Aware Topologies
4
Notes: My vision is that networks should become flexible and demand-aware.

## Slide 8: Our Vision Flexible and Demand-Aware Topologies
4
1
2
3
4
5
6
7
8
e.g.,
mirrors
new flexible
interconnect
Notes: e.g., based on mirrors.

## Slide 9: Our Vision Flexible and Demand-Aware Topologies
4
1
2
3
4
5
6
7
8
e.g.,
mirrors
new flexible
interconnect
demand
matrix:
Notes: For example, if the demand matrix looks like this: 1 communicates to 5, 2 to 6, etc…

## Slide 10: Our Vision Flexible and Demand-Aware Topologies
4
1
2
3
4
5
6
7
8
Matches demand
demand
matrix:
e.g.,
mirrors
new flexible
interconnect
Notes: … it makes sense to interconnect the servers like this.
This perfectly matches the demand.

## Slide 11: Our Vision Flexible and Demand-Aware Topologies
4
1
2
3
4
5
6
7
8
new
demand:
e.g.,
mirrors
new flexible
interconnect
Notes: If the demand changes to this…

## Slide 12: Our Vision Flexible and Demand-Aware Topologies
4
1
2
3
4
5
6
7
8
new
demand:
Matches demand
e.g.,
mirrors
new flexible
interconnect
Notes: … the topology should be changed as well, to match the demand again.

## Slide 13: Our Vision Flexible and Demand-Aware Topologies
4
1
2
3
4
5
6
7
8
Self-Adjusting
Networks
new
demand:
e.g.,
mirrors
new flexible
interconnect
Notes: This is the idea of self-adjusting networks: they dynamically reconfigure over time, in a demand-aware manner.

## Slide 14: Our Motivation Much Structure in the Demand
5
My hypothesis: can be exploited.
Empirical studies:
sources
destinations
Facebook
sources
destinations
Microsoft
traffic bursty over time
Mbps
Facebook
Time (seconds)
traffic matrices sparse and skewed
Notes: My motivation for this project is that there is much structure in the demand indeed.
Empirical studies show that traffic matrices are sparse and skewed, and traffic bursty over time.
My hypothesis is that this can be exploited.

## Slide 15: Recent Representation of Trace Structure: Complexity Map
pF
CNS
ML
DB
Web
Had
Multi
Grid
NN
Griner et al., SIGMETRICS 2020

## Slide 16: Recent Representation of Trace Structure: Complexity Map
non-temporal complexity
pF
CNS
ML
DB
Web
Had
Multi
Grid
temporal complexity
bursty
uniform
bursty & skewed
skewed
NN
Griner et al., SIGMETRICS 2020
pF
CNS
ML
DB
Web
Had
Multi
Grid
NN
Different structures!

## Slide 17: Sounds Crazy? Emerging Enabling Technology.
7
H2020:
“Photonics one of only five
key enabling technologies for future prosperity.”
US National Research Council:
“Photons are the new
Electrons.”
Photonics
Notes: Generally, photonics is seen as one of the key enabling technologies of our future prosperity, both in the EU and in the US.

## Slide 18: Enabler Novel Reconfigurable Optical Switches
8
⇢ Spectrum of prototypes
⇀ Different sizes, different reconfiguration times
⇀ From our last year’s ACM SIGCOMM workshop OptSys
Prototype 1
Prototype 2
Prototype 3
Notes: More specifically, the enabler for our project are reconfigurable optical switches.
There is currently a spectrum of prototypes emerging: these prototypes have different sizes, different reconfiguration times, etc.
Here are some examples from the SIGCOMM workshop we organized last month.

## Slide 19: Example Optical Circuit Switch
⇢ Optical Circuit Switch rapid adaption of physical layer
⇀ Based on rotating mirrors
Optical Circuit Switch By Nathan Farrington, SIGCOMM 2010
Lenses
Fixed
Mirror
Mirrors on Motors
Rotate Mirror
9
Notes: More specifically, the enabler for our project are reconfigurable optical switches.
There is currently a spectrum of prototypes emerging: these prototypes have different sizes, different reconfiguration times, etc.
Here are some examples from the SIGCOMM workshop we organized last month.

## Slide 20: The Big Picture
10
Flexibility
Structure
Efficiency
New!
More!
Self-Adjusting
Networks
Now is the time!
Notes: In a nutshell, the idea of this project is to exploit these new technological flexibilities, as well as the structure in the demand, to design self-adjusting networks, and improve efficiency. Now is the right time for this project:
it is possible to have impact as the community is currently re-achritecting networks anyways.

## Slide 21: The Big Picture
Flexibility
Structure
Efficiency
New!
More!
Self-Adjusting
Networks
Now is the time!
Our goal: Develop the theoretical foundations of demand-aware, self-adjusting networks.
10
Notes: Our goal is to develop the theoretical foundations of such demand-aware networks, and a framework which comes with provable guarantees.

## Slide 22: Unique Position Demand-Aware, Self-Adjusting Systems
Everywhere, but mainly
in software
Our focus:
in hardware
vs
Algorithmic trading
Neural networks
Recommender systems
11
Notes: The project assumes an interesting position: today there are many self-adjusting systems, e.g., in algorithmic trading, recommender systems, or also neural networks of course.
These systems are in software only.
In contrast, we aim to build self-adjusting systems in hardware, on the physical layer.

## Slide 23: The Natural Question: Given This Structure, What Can Be Achieved? Metrics and Algorithms?
12
A first insight: entropy of the demand.
Notes: Of course, we are particularly interested in what can be achieved in self-adjusting networks.
To this end, we want to develop metrics for self-adjusting networks which depend on the demand, as well as algorithms.
Here we have some first insights that the entropy of the demand can serve as a useful metric for self-adjusting networks.

## Slide 24: Our Insight: Connection to Datastructures
13
Traditional BST
Demand-aware BST
Self-adjusting BST
More structure: improved access cost
Notes: One approach in this project is to exploit a connection to self-adjusting datastructures.
We know today that the more structure there is in an access pattern to a datastructure, the more we can improve the access cost if we make the datastructure more demand-aware and self-adjusting.

## Slide 25: Our Insight: Connection to Datastructures & Coding
13
Traditional BST
(Worst-case coding)
Demand-aware BST
(Huffman coding)
Self-adjusting BST
(Dynamic Huffman coding)
More structure: improved access cost / shorter codes
Notes: Similar benefits exist also for coding, by the way.

## Slide 26: Our Insight: Connection to Datastructures & Coding
13
Traditional BST
(Worst-case coding)
Demand-aware BST
(Huffman coding)
Self-adjusting BST
(Dynamic Huffman coding)
More structure: improved access cost / shorter codes
Similar benefits?
Notes: With our research we want to investigate whether similar benefits can be obtained in self-adjusting networks as well.

## Slide 27: Our Insight: Connection to Datastructures & Coding
13
Traditional BST
(Worst-case coding)
Demand-aware BST
(Huffman coding)
Self-adjusting BST
(Dynamic Huffman coding)
More structure: improved access cost / shorter codes
More than
an analogy!
Similar benefits?
Notes: However, this is more than an analogy.

## Slide 28: Our Insight: Connection to Datastructures & Coding
13
Traditional BST
(Worst-case coding)
Demand-aware BST
(Huffman coding)
Self-adjusting BST
(Dynamic Huffman coding)
More than
an analogy!
Reduced expected route lengths!
entropy
rate
entropy
log n
entropy
rate
entropy
log n
Generalize methodology:
... and transfer entropy bounds and algorithms of data-structures to networks.
First result:
Demand-aware networks of asymptotically optimal route lengths.
Notes: Actually, we also have first results on how we can exploit algorithms from coding and datastructures to design self-adjusting networks which match these lower bounds and are hence asymptotically optimal.

## Slide 29: It is more complicated…
⇀ Self-adjusting networks may be really useful to serve large
flows (elephant flows): avoiding multi-hop routing
6 hops
1 hop
vs
14

## Slide 30: It is more complicated…
⇀ Self-adjusting networks may be really useful to serve large
flows (elephant flows): avoiding multi-hop routing
6 hops
1 hop
vs
bandwidth
tax!
14

## Slide 31: It is more complicated…
⇀ Self-adjusting networks may be really useful to serve large
flows (elephant flows): avoiding multi-hop routing
⇀ However, requires optimization and adaption, which takes time
6 hops
1 hop
vs
bandwidth
tax!
14

## Slide 32: It is more complicated…
⇀ Self-adjusting networks may be really useful to serve large
flows (elephant flows): avoiding multi-hop routing
⇀ However, requires optimization and adaption, which takes time
vs
6 hops
1 hop
bandwidth
tax!
latency
tax!
14

## Slide 33: Indeed, it is more complicated than that… Challenge: Traffic Diversity
Diverse patterns:
⇀ Shuffling/Hadoop:
all-to-all
⇀ All-reduce/ML: ring or
tree traffic patterns
⇀ Elephant flows
⇀ Query traffic: skewed
⇀ Mice flows
⇀ Control traffic: does not evolve
but has non-temporal structure
Diverse requirements:
⇀ ML is bandwidth hungry,
small flows are latency-
sensitive
15

## Slide 34
Opportunity: Tech Diversity
Demand- oblivious
Demand- aware
Diverse topology components:
⇀ demand-oblivious and
demand-aware
⇀ static vs dynamic
16

## Slide 35
Static
Demand- oblivious
Demand- aware
Dynamic
Diverse topology components:
⇀ demand-oblivious and
demand-aware
⇀ static vs dynamic
Opportunity: Tech Diversity
16

## Slide 36
Static
Demand- oblivious
Demand- aware
Dynamic
e.g., RotorNet (SIGCOMM‘17), Opera (NSDI‘20), Sirius (SIGCOMM‘20)
e.g., FireFly (SIGCOMM‘14), ProjecToR (SIGCOMM‘16), SplayNet (ToN‘16)
e.g., Clos (SIGCOMM‘08), Slim Fly (SC‘14), Xpander (SIGCOMM‘17)
Diverse topology components:
⇀ demand-oblivious and
demand-aware
⇀ static vs dynamic
Opportunity: Tech Diversity
16

## Slide 37
Static
Demand- oblivious
Demand- aware
Dynamic
Rotor
Demand-Aware
Static
Diverse topology components:
⇀ demand-oblivious and
demand-aware
⇀ static vs dynamic
Opportunity: Tech Diversity
16

## Slide 38
Static
Demand- oblivious
Demand- aware
Dynamic
Which approach is best?
Rotor
Demand-Aware
Static
Diverse topology components:
⇀ demand-oblivious and
demand-aware
⇀ static vs dynamic
Opportunity: Tech Diversity
16

## Slide 39
Static
Demand- oblivious
Demand- aware
Dynamic
Which approach is best?
As always in CS: It depends…
Rotor
Demand-Aware
Static
Diverse topology components:
⇀ demand-oblivious and
demand-aware
⇀ static vs dynamic
Opportunity: Tech Diversity
16

## Slide 40
Rack Interconnect
1
2
3
4
5
6
7
8
Typical rack internconnect: ToR-Matching-ToR (TMT) model
Optical Switches
17

## Slide 41
Rack Interconnect
1
2
3
4
5
6
7
8
Typical rack internconnect: ToR-Matching-ToR (TMT) model
…
S1
S2
Sk
17

## Slide 42: Details: Switch Types Periodic Switch (aka Rotor Switch)
Rotor switch: periodic matchings (demand-oblivious)
time
M1
M2
M3
M1
M2
M3
Si:
18

## Slide 43: Details: Switch Types Demand-Aware Switch
Demand-aware switch: optimized matchings
Si:
time
M1
M3
M2
M2
M1
M1
19

## Slide 44: Details: Switch Types Static Switch
Static switches: combine for optimized static topology
S1:
M1
M2
M3
S2:
S3:
e.g, tree, expander
20

## Slide 45: Design Tradeoffs (1) The “Awareness-Dimension”
Demand- oblivious
Demand- aware
Rotor
Demand-Aware
Good for all-to-all traffic!
⇀ oblivious: very fast
periodic direct connectivity
⇀ no control plane overhead
Good for elephant flows!
⇀ optimizable toward traffic
⇀ but slower
21

## Slide 46: Design Tradeoffs (1) The “Awareness-Dimension”
Demand- oblivious
Demand- aware
Rotor
Demand-Aware
Good for all-to-all traffic!
⇀ oblivious: very fast
periodic direct connectivity
⇀ no control plane overhead
Good for elephant flows!
⇀ optimizable toward traffic
⇀ but slower
Compared to static networks: latency tax!
low tax
high tax
21

## Slide 47: Design Tradeoffs (2) The “Flexibility-Dimension”
Static
Dynamic
Rotor /
Demand-Aware
Clos
Good for high throughput!
⇀ direct connectivity saves
bandwidth along links
Good for low latency!
⇀ no need to wait for
reconfigurable links
⇀ compared to dynamic:
bandwidth tax (multi-hop)
22

## Slide 48: Design Tradeoffs (2) The “Flexibility-Dimension”
Static
Dynamic
Rotor /
Demand-Aware
Clos
Good for high throughput!
⇀ direct connectivity saves
bandwidth along links
Good for low latency!
⇀ no need to wait for
reconfigurable links
⇀ compared to dynamic:
bandwidth tax (multi-hop)
bandwidth
tax
latency
tax
22

## Slide 49
First Observations
⇢ Observation 1: Different topologies provide
different tradeoffs.
⇢ Observation 2: Different traffic requires different
topology types.
⇢ Observation 3: A mismatch of demand and topology
can increase flow completion times.
⇀ bad idea: serving mice flows on Rotor topology
⇀ bad idea: serving elephant flows on static topology
23

## Slide 50
Examples:
Match or Mismatch?
Shuffling
ML
Delay sensitive
Telemetry / control
Demand
Static
Demand- oblivious
Demand- aware
Dynamic
Rotor
Demand-Aware
Static
Topology
24

## Slide 51
Examples:
Match or Mismatch?
Shuffling
ML
Delay sensitive
Telemetry / control
Demand
Static
Demand- oblivious
Demand- aware
Dynamic
Rotor
Demand-Aware
Static
Topology
Serving mice flows on demand-aware?
?
24

## Slide 52
Examples:
Match or Mismatch?
Shuffling
ML
Delay sensitive
Telemetry / control
Demand
Static
Demand- oblivious
Demand- aware
Dynamic
Rotor
Demand-Aware
Static
Topology
Serving mice flows on demand-aware?
Bad idea! Latency tax.
?
24

## Slide 53
Examples:
Match or Mismatch?
Shuffling
ML
Delay sensitive
Telemetry / control
Demand
Static
Demand- oblivious
Demand- aware
Dynamic
Rotor
Demand-Aware
Static
Topology
Serving elephant flows on static?
?
24

## Slide 54
Examples:
Match or Mismatch?
Shuffling
ML
Delay sensitive
Telemetry / control
Demand
Static
Demand- oblivious
Demand- aware
Dynamic
Rotor
Demand-Aware
Static
Topology
Serving elephant flows on static? Bad idea! Bandwidth tax.
?
24

## Slide 55
Cerberus:
Shuffling
ML
Delay sensitive
Telemetry / control
Static
Demand- oblivious
Demand- aware
Dynamic
Our system Cerberus* serves traffic on the “best topology”!
* Griner et al., ACM SIGMETRICS 2022

## Slide 56
⇢ Observation 1: Different apps have different flow size distributions.
⇢ Observation 2: The transmission time of a flow depends on its size.
⇢ Observation 3: For small flows, flow completion time suffers if
network needs to be reconfigured first.
⇢ Observation 4: For large flows, reconfiguration time may amortize.
Flow Size Matters
25

## Slide 57
⇢ Observation 1: Different apps have different flow size distributions.
⇢ Observation 2: The transmission time of a flow depends on its size.
⇢ Observation 3: For small flows, flow completion time suffers if
network needs to be reconfigured first.
⇢ Observation 4: For large flows, reconfiguration time may amortize.
Flow Size Matters
25

## Slide 58
⇢ Observation 1: Different apps have different flow size distributions.
⇢ Observation 2: The transmission time of a flow depends on its size.
⇢ Observation 3: For small flows, flow completion time suffers if
network needs to be reconfigured first.
⇢ Observation 4: For large flows, reconfiguration time may amortize.
Flow Size Matters
25

## Slide 59
⇢ Observation 1: Different apps have different flow size distributions.
⇢ Observation 2: The transmission time of a flow depends on its size.
⇢ Observation 3: For small flows, flow completion time suffers if
network needs to be reconfigured first.
⇢ Observation 4: For large flows, reconfiguration time may amortize.
Flow Size Matters
25

## Slide 60
Cerberus
1
2
3
4
5
6
7
8
Optical Switches
26

## Slide 61
Cerberus
1
2
3
4
5
6
7
8
Ks
static
switches
Kr
rotor
switches
Kd
demand-aware
switches
26

## Slide 62
Cerberus
1
2
3
4
5
6
7
8
Ks
static
switches
Kr
rotor
switches
Kd
demand-aware
switches
Scheduling: Small flows go via static switches…
26

## Slide 63
Cerberus
1
2
3
4
5
6
7
8
Ks
static
switches
Kr
rotor
switches
Kd
demand-aware
switches
Scheduling: … medium flows via rotor switches…
26

## Slide 64
Cerberus
1
2
3
4
5
6
7
8
Ks
static
switches
Kr
rotor
switches
Kd
demand-aware
switches
Scheduling: … and large flows via demand-aware switches
(if one available, otherwise via rotor).
26

## Slide 65
Throughput Analysis
Demand Matrix
Metric: throughput of a demand matrix…
27

## Slide 66
Throughput Analysis
Demand Matrix
… is the maximal scale down factor by which traffic is feasible.
Metric: throughput of a demand matrix…
27

## Slide 67
Throughput Analysis
Demand Matrix
… is the maximal scale down factor by which traffic is feasible.
Metric: throughput of a demand matrix…
27

## Slide 68
Throughput Analysis
BW & latency tax!
BW tax!
Demand Matrix
Worst demand matrix for static and rotor: permutation. Best case for demand-aware!
27
Notes: throughput = theta factor we multiply demand => scale it down so we can send it over topology: throughput of a matrix on a given topology. for each demand we have a factor.
matrix is saturated
permutation matrix: is worst case for expander (pay much bandwidth tax), also worst for RotorNet
for demandaware it is the best
this is the worst case but what about real traffic?
depends on specific parameter of datamining
note

## Slide 69
Completion Time
Data mining workload
⇢ Demand completion time: How long does
it take to serve a demand matrix?
⇢ Also useful in analysis: throughput can be computed more
easily via demand completion time.
28
Notes: What about the methodology of finding throughput via demand completion time? When we know demand-completion time we can bound the throughput. Simpler to compute completion time, because can account for watiting time / tax easier,

## Slide 70: Conclusion
⇢ Diverse traffic requires
diverse technologies
⇢ Cerberus aims to assign
traffic to its best topology
⇀ Depending on flow size
⇢ Many challenges
⇀ Impact on routing and congestion control
⇀ Sensitivity analysis
⇀ Prototyping
Thank you!
29

## Slide 71
http://self-adjusting.net/
Project website
https://trace-collection.net/
Trace collection website
Websites
Notes: Over the last years, we have worked on flexible routing (enabled by SDN) and flexible resource allocation and service embedding (enabled by virtualization).
With this project, we want to tackle the physical layer, enabled by emerging optical technologies.

## Slide 72
Static DAN
Static Optimality
Overview: Models
Dynamic DAN
Robust DAN
Concurrent DANs
Further Reading
Notes: The potential gain can be significant.

## Slide 73: Selected References
On the Complexity of Traffic Traces and Implications
Chen Avin, Manya Ghobadi, Chen Griner, and Stefan Schmid.
ACM SIGMETRICS, Boston, Massachusetts, USA, June 2020.
Survey of Reconfigurable Data Center Networks: Enablers, Algorithms, Complexity Klaus-Tycho Foerster and Stefan Schmid. SIGACT News, June 2019.
Toward Demand-Aware Networking: A Theory for Self-Adjusting Networks (Editorial) Chen Avin and Stefan Schmid. ACM SIGCOMM Computer Communication Review (CCR), October 2018.
Dynamically Optimal Self-Adjusting Single-Source Tree Networks Chen Avin, Kaushik Mondal, and Stefan Schmid.
14th Latin American Theoretical Informatics Symposium (LATIN), University of Sao Paulo, Sao Paulo, Brazil, May 2020.
Demand-Aware Network Design with Minimal Congestion and Route Lengths Chen Avin, Kaushik Mondal, and Stefan Schmid. 38th IEEE Conference on Computer Communications (INFOCOM), Paris, France, April 2019. Distributed Self-Adjusting Tree Networks Bruna Peres, Otavio Augusto de Oliveira Souza, Olga Goussevskaia, Chen Avin, and Stefan Schmid. 38th IEEE Conference on Computer Communications (INFOCOM), Paris, France, April 2019.
Efficient Non-Segregated Routing for Reconfigurable Demand-Aware Networks Thomas Fenz, Klaus-Tycho Foerster, Stefan Schmid, and Anaïs Villedieu. IFIP Networking, Warsaw, Poland, May 2019.
DaRTree: Deadline-Aware Multicast Transfers in Reconfigurable Wide-Area Networks Long Luo, Klaus-Tycho Foerster, Stefan Schmid, and Hongfang Yu. IEEE/ACM International Symposium on Quality of Service (IWQoS), Phoenix, Arizona, USA, June 2019.
Demand-Aware Network Designs of Bounded Degree Chen Avin, Kaushik Mondal, and Stefan Schmid. 31st International Symposium on Distributed Computing (DISC), Vienna, Austria, October 2017.
SplayNet: Towards Locally Self-Adjusting Networks Stefan Schmid, Chen Avin, Christian Scheideler, Michael Borokhovich, Bernhard Haeupler, and Zvi Lotker. IEEE/ACM Transactions on Networking (TON), Volume 24, Issue 3, 2016. Early version: IEEE IPDPS 2013.
Characterizing the Algorithmic Complexity of Reconfigurable Data Center Architectures Klaus-Tycho Foerster, Monia Ghobadi, and Stefan Schmid. ACM/IEEE Symposium on Architectures for Networking and Communications Systems (ANCS), Ithaca, New York, USA, July 2018.
Notes: Over the last years, we have worked on flexible routing (enabled by SDN) and flexible resource allocation and service embedding (enabled by virtualization).
With this project, we want to tackle the physical layer, enabled by emerging optical technologies.

## Slide 74: Bonus Material
Hogwarts Stair
Notes: Over the last years, we have worked on flexible routing (enabled by SDN) and flexible resource allocation and service embedding (enabled by virtualization).
With this project, we want to tackle the physical layer, enabled by emerging optical technologies.

## Slide 75: Bonus Material
Golden Gate Zipper
Notes: Over the last years, we have worked on flexible routing (enabled by SDN) and flexible resource allocation and service embedding (enabled by virtualization).
With this project, we want to tackle the physical layer, enabled by emerging optical technologies.

## Slide 76: Bonus Material
In HPC
Notes: Over the last years, we have worked on flexible routing (enabled by SDN) and flexible resource allocation and service embedding (enabled by virtualization).
With this project, we want to tackle the physical layer, enabled by emerging optical technologies.

## Slide 77: Question: How to Quantify such “Structure” in the Demand?
Notes: Let me give you an idea of the questions and approach used in our project.
A first most basic question regards how we can quantify the structure in the demand.

## Slide 78
Intuition Which demand has more structure?
vs
Color = communication pair
⇢ Traffic matrices of two different distributed ML applications
⇀ GPU-to-GPU
vs
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 79
Intuition Which demand has more structure?
vs
⇢ Traffic matrices of two different distributed ML applications
⇀ GPU-to-GPU
Color = communication pair
More uniform
More structure
vs
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 80
Intuition Spatial vs temporal structure
⇢ Two different ways to generate same traffic matrix:
⇀ Same non-temporal structure
⇢ Which one has more structure?
vs
vs
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 81
Intuition Spatial vs temporal structure
⇢ Two different ways to generate same traffic matrix:
⇀ Same non-temporal structure
⇢ Which one has more structure?
Systematically?
vs
vs
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 82
Trace Complexity Information-Theoretic Approach
“Shuffle&Compress”
Time
Original
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 83
Trace Complexity Information-Theoretic Approach
“Shuffle&Compress”
Randomize rows
Uniform
More structure (compresses better)
Increasing complexity (systematically randomized)
Original
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 84
Trace Complexity Information-Theoretic Approach
“Shuffle&Compress”
Randomize rows
Uniform
Original
Remove non-temp.
Remove temporal
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 85
Trace Complexity Information-Theoretic Approach
“Shuffle&Compress”
Difference in size (entropy)?
Randomize rows
Uniform
Original
Remove non-temp.
Remove temporal
Compress
Shuffle
Difference in size (entropy)?
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 86
Trace Complexity Information-Theoretic Approach
“Shuffle&Compress”
Difference in size (entropy)?
Randomize rows
Uniform
Original
Remove non-temp.
Remove temporal
Compress
Shuffle
Difference in size (entropy)?
Can be used to define 2-dimensional complexity map!
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 87: Our Methodology Complexity Map
bursty
uniform
non-temporal complexity
temporal complexity
No structure
bursty & skewed
skewed
Our approach: iterative randomization and compression of trace to identify dimensions of structure.
Notes: We believe that an information-theoretic approach can provide interesting insights here.
As a first approach, we have used iterative randomization and compression to identify the different dimensions of structure.
The resulting complexity map looks like this: On the x-axis, there is the temporal complexity, on the y-axis the non-temporal. Workloads without any structure end up on the upper right.

## Slide 88: Our Methodology Complexity Map
non-temporal complexity
pF
CNS
ML
DB
Web
Had
Multi
Grid
temporal complexity
Different structures!
bursty
uniform
bursty & skewed
skewed
NN
No structure
Our approach: iterative randomization and compression of trace to identify dimensions of structure.
Notes: When mapping different applications, we can see that they end up at different locations: they have different amounts of temporal and non-temporal structures.

## Slide 89: Our Methodology Complexity Map
non-temporal complexity
pF
CNS
ML
DB
Web
Had
Multi
Grid
temporal complexity
Potential gain!
bursty & skewed
skewed
bursty
uniform
NN
Different structures!
Our approach: iterative randomization and compression of trace to identify dimensions of structure.
Notes: The potential gain can be significant.

## Slide 90: Further Reading ACM SIGMETRICS 2020
Notes: The potential gain can be significant.

## Slide 91: Case Study “Route Lengths” Constant-Degree Demand-Aware Network
Sources
Destinations
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
1
2
3
4
5
6
7
1
2
3
4
5
6
7
2
1
3
4
5
6
7
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 92: Case Study “Route Lengths” Constant-Degree Demand-Aware Network
Sources
Destinations
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Much from 4 to 5
Add link
1
2
3
4
5
6
7
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 93: Case Study “Route Lengths” Constant-Degree Demand-Aware Network
1
3
4
5
6
7
Sources
Destinations
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Communicated with many
indirect
2
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 94: Case Study “Route Lengths” Constant-Degree Demand-Aware Network
1
3
4
5
6
7
Sources
Destinations
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Don’t
communicate
Makes sense
2
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 95: Algorithm: Idea
Sources
Destinations
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
0 |  |  |  |  |  | 
 | 0 |  | 0 | 0 | 0 | 
 |  | 0 |  | 0 | 0 | 
 | 0 |  | 0 |  | 0 | 0
 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 0 |  | 0
1
2
3
4
5
6
1
2
3
4
5
6
7
Huffman tree:
“ego-tree”
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 96: Entropy Upper Bound
⇢ Idea for algorithm:
⇀ union of trees
⇀ reduce degree
⇀ but keep distances
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 97: Entropy Upper Bound
⇢ Idea for algorithm:
⇀ union of trees
⇀ reduce degree
⇀ but keep distances
⇢ Ok for sparse demands
⇀ not everyone gets tree
⇀ helper nodes
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 98: Entropy Upper Bound
⇢ Idea for algorithm:
⇀ union of trees
⇀ reduce degree
⇀ but keep distances
⇢ Ok for sparse demands
⇀ not everyone gets tree
⇀ helper nodes
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 99: Entropy Upper Bound
⇢ Idea for algorithm:
⇀ union of trees
⇀ reduce degree
⇀ but keep distances
⇢ Ok for sparse demands
⇀ not everyone gets tree
⇀ helper nodes
Static
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 100: Intuition of Algorithm
Demand graph:
Demand-aware network:
Ego-trees for large nodes
Helper node
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 101: Entropy Lower Bound
ERL=Ω(H(Y|X))
destinations
sources
degree
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 102: Dynamic Algorithm
Dynamic
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 103: Further Reading TON 2016, DISC 2017, CCR 2019, INFOCOM 2019
Notes: The potential gain can be significant.

## Slide 104: Related Problem Virtual Network Embedding Problem (VNEP)
Embedding?
Example △=2: A Minium Linear Arrangement (MLA) Problem
⇀ Minimizes sum of virtual
edges
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 105: Related Problem Virtual Network Embedding Problem (VNEP)
cost 5
Bad!
Example △=2: A Minium Linear Arrangement (MLA) Problem
⇀ Minimizes sum of virtual
edges
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 106: Related Problem Virtual Network Embedding Problem (VNEP)
cost 1
Good!
Example △=2: A Minium Linear Arrangement (MLA) Problem
⇀ Minimizes sum of virtual
edges
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 107: Related Problem Virtual Network Embedding Problem (VNEP)
Example △=2: A Minium Linear Arrangement (MLA) Problem
⇀ Minimizes sum of virtual
edges
MLA is NP-hard
⇀ … and so is our problem!
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 108: Related Problem Virtual Network Embedding Problem (VNEP)
Example △=2: A Minium Linear Arrangement (MLA) Problem
⇀ Minimizes sum of virtual
edges
MLA is NP-hard
⇀ … and so is our problem!
But what about △>2?
⇀ Embedding problem still hard
⇀ But we have a new degree of
freedom!
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.

## Slide 109: Related Problem Virtual Network Embedding Problem (VNEP)
Example △=2: A Minium Linear Arrangement (MLA) Problem
⇀ Minimizes sum of virtual
edges
MLA is NP-hard
⇀ … and so is our problem!
But what about △>2?
⇀ Embedding problem still hard
⇀ But we have a new degree of
freedom!
Simplifies problem?!
Notes: So far, we have just scratched the surface, and with this ERC project, we want to explore the rest of the iceberg.
Indeed, the notion of self-adjusting networks opens are large uncharted field, with many questions.
We structure our project around models and metrics, algorithms, fault-tolerance, integration into higher layers, and case studies.
In particular, we will explore metrics and algorithms for by how much load can be lowered, energy reduced and quality-of-service improved in selfadjusting networks.
We also need to develop models for the tradeoff between the benefits and costs of reconfigurations over time.
We also study how self-adjusting networks can be used to improve fault-tolerance, what is the impact on other layers, and how to apply our solutions in a specific case study, e.g., how to develop a scalable control plane.
This project hence requires expertises from different fields, from networking, over distributed systems, algorithms, to performance evaluation.
I have the necessary background in all these areas.