## Slide 1
Anton Juerss and Stefan Schmid

## Slide 2
All-to-All: everyone sends to everyone
Training and inference require synchronizations across accelerators
Example: All-to-All — each node sends a unique message to every other node
Notes: Training and inference require synchronizations across accelerators Collective primitives define initial/final synchronization state
Collective algorithms realize primitives in communication phases
Example: All-to-All Primitive each node sends a unique message to every other node
Pairwise algorithm: each message is routed via shortest path

## Slide 3
All-to-All: everyone sends to everyone
Training and inference require synchronizations across accelerators
Example: All-to-All — each node sends a unique message to every other node
All-to-All cost grow linearly with n in rings topologies with network size
Notes: Training and inference require synchronizations across accelerators Collective primitives define initial/final synchronization state
Collective algorithms realize primitives in communication phases
Example: All-to-All Primitive each node sends a unique message to every other node
Pairwise algorithm: each message is routed via shortest path

## Slide 4
All-to-All: everyone sends to everyone
Training and inference require synchronizations across accelerators
Example: All-to-All — each node sends a unique message to every other node
All-to-All cost grow linearly with n in rings topologies with network size
Can we use reconfigurable networks to fix this problem?
All-to-All cost grow linearly with n in rings topologies with network size
Notes: Training and inference require synchronizations across accelerators Collective primitives define initial/final synchronization state
Collective algorithms realize primitives in communication phases
Example: All-to-All Primitive each node sends a unique message to every other node
Pairwise algorithm: each message is routed via shortest path

## Slide 5
Collectives match reconfigurable networks
Collectives naturally offer:
Known demand matrices
Node synchronization between phases
Concurrent transmissions have equal cost
Natural opportunities to reconfigure

## Slide 6
Collectives match reconfigurable networks
Collectives naturally offer:
Known demand matrices
Node synchronization between phases
Concurrent transmissions have equal cost
Natural opportunities to reconfigure
K=0
K=1
K=2
K=0,1,2,...
Common reconfiguration approaches:
One-shot: before collective operations
Dynamic: between each collective phases

## Slide 7
Optimization problem
Reconfiguration is global: every node waits for a delay (µs … ms)

## Slide 8
Optimization problem
Reconfiguration is global: every node waits for a delay (µs … ms)
1 Matching: no connected topology + every-step reconfigurations
Phase 0
Phase 1
Phase 2

## Slide 9
Optimization problem
Reconfiguration is global: every node waits for a delay (µs … ms)
1 Matching: no connected topology + every-step reconfigurations 2 Matchings: OCS with 2n ports = every node keeps degree two ⇒ feasible topologies are rings
Ring topology
Small subrings

## Slide 10
Optimization problem
Reconfiguration is global: every node waits for a delay (µs … ms)
1 Matching: no connected topology + every-step reconfigurations 2 Matchings: OCS with 2n ports = every node keeps degree two ⇒ feasible topologies are rings
Following number of reconfigurations:
1 Matching with s phases ⇒ reconfigurations with
2 Matchings ⇒ reusable topology states number of reconfigurations
Observation: 1. fewer phases require fewer reconfigurations
2. reusable reconfiguration states ⇒ amortized better

## Slide 11
Challenges in reconfigurable All-to-All
Pairwise A2A: each node sends block directly to its destination

## Slide 12
Challenges in reconfigurable All-to-All
Pairwise A2A: each node sends block directly to its destination
Option 1: one step with all simultaneous communication
Transmissions from node 0

## Slide 13
Challenges in reconfigurable All-to-All
Pairwise A2A: each node sends block directly to its destination
Option 1: one step with all simultaneous communication Option 2: steps with single block transmissions
Step 0
Step 1
Step 2
Step 3

## Slide 14
Step 0
Step 1
Step 2
Step 3
Challenges in reconfigurable All-to-All
Pairwise A2A: each node sends block directly to its destination
Option 1: one step with all simultaneous communication Option 2: steps single block transmission
Observation: Both implementations are not feasible for reconfigurable networks

## Slide 15
Bruck‘s algorithm for reconfigurable networks
Bruck et al. (1994): All-to-All in phases by aggregating blocks

## Slide 16
Bruck‘s algorithm for reconfigurable networks
Bruck et al. (1994): All-to-All in phases by aggregating blocks
Built for a multiport message-passing model, not for reconfigurable networks

## Slide 17
Bruck‘s algorithm for reconfigurable networks
Bruck et al. (1994): All-to-All in phases by aggregating blocks
Built for a multiport message-passing model, not for reconfigurable networks
Phase k: node u sends to ⇒ one logical direction only
Phase 0
Phase 1
Phase 2

## Slide 18
Bruck‘s algorithm for reconfigurable networks
Bruck et al. (1994): All-to-All in phases by aggregating blocks
Built for a multiport message-passing model, not for reconfigurable networks
Phase k: node u sends to ⇒ one logical direction only
With 2n ports: 2 sends + 2 receives ⇒ would require four links per node

## Slide 19
Bruck‘s algorithm for reconfigurable networks
Bruck et al. (1994): All-to-All in phases by aggregating blocks
Built for a multiport message-passing model, not for reconfigurable networks
Phase k: node u sends to ⇒ one logical direction only
With 2n ports: 2 sends + 2 receives ⇒ would require four links per node
Mirroring Bruck restores feasibility — but still phases

## Slide 20
ReTri: Reconfigurable Trivance
Recently proposed algorithm to reduce phases ⇒ Trivance
Phase k: node sends to and
18th August SIGCOMM 1:50 PM Research Session 3

## Slide 21
ReTri: Reconfigurable Trivance
Recently proposed algorithm to reduce phases ⇒ Trivance
Phase k: node sends to and
Two peers per phase ⇒ matches the two optical links per node
Symmetric exchange ⇒ both directions per optical link are used
All-to-All completes in communication phases
Phase 0
Phase 1
Case: Topology remains static

## Slide 22
ReTri: Reconfigurable Trivance
Recently proposed algorithm to reduce phases ⇒ Trivance
Phase k: node sends to and
Two peers per phase ⇒ matches the two optical links per node
Symmetric exchange ⇒ both directions per optical link are used
All-to-All completes in communication phases
Phase 0
Communication pattern
+
Topology reconfiguration
Case: Reconfiguration

## Slide 23
ReTri: Reconfigurable Trivance
Recently proposed algorithm to reduce phases ⇒ Trivance
Phase k: node sends to and
Two peers per phase ⇒ matches the two optical links per node
Symmetric exchange ⇒ both directions per optical link are used
All-to-All completes in communication phases
Phase 0
Phase 1
Case: Reconfiguration
Minimal communication cost

## Slide 24
ReTri: block propagation
In phase k, each block moves or or stays local
Each source-destination pair has unique power of three representation
Phase 0
Phase 1
Block propagation from node 0 to node 7:

## Slide 25
ReTri: ternary subrings
In phase k, each block moves or or stays local
Each source-destination pair has unique power of three representation
Peers in phase k are ⇒ same residue class modulo
Later offsets are multiples of ⇒ future peers are in the same subset
  ⇒ partition in subrings of
Phase 0
Phase 1

## Slide 26
Reconfiguration: reuse instead of repeat
After reconfiguring for phase k, both peers are directly connected
Future peers remain inside the same subring: 3k+t hops become 3t hops
⇒ one reconfiguration can serve several phases
ReTri needs ≈ 1.58× fewer phases than Bruck

## Slide 27
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Trivance vs. Reconf. Bruck
Trivance vs. Static

## Slide 28
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Trivance vs. Reconf. Bruck
Trivance vs. Static
Speedup increases vs. Static with message size

## Slide 29
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Trivance vs. Reconf. Bruck
Trivance vs. Static
Speedup increases vs. Static with message size
Higher ⇒ fewer reconfigurations

## Slide 30
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Trivance vs. Reconf. Bruck
Trivance vs. Static
Speedup increases vs. Static with message size
Higher ⇒ fewer reconfigurations
Improvement is constant

## Slide 31
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Trivance vs. Reconf. Bruck
Trivance vs. Static
Speedup increases vs. Static with message size
Higher ⇒ fewer reconfigurations
Improvement is constant
Without reconfigs. ReTri still improves Bruck

## Slide 32
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Network size = 8/9
Network size = 256/243
Continuous improvement over Bruck by 1.3-2.2

## Slide 33
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Network size = 8/9
Network size = 256/243
Continuous improvement over Bruck by 1.7-2.2
Larger networks = larger speedups

## Slide 34
Simulation with Astra-Sim/ns-3
Astra-Sim + ns-3 · 400 Gb/s links · 1 µs link latency · 1.7 µs per phase latency · Messages 1 KB – 256 MB · = 100ns – 50 ms · ReTri n = 81 vs. Bruck n = 64
Network size = 8/9
Network size = 256/243
Continuous improvement over Bruck by 1.7-2.2
Larger networks = larger speedups
ReTri can improve static All-to-All for 256MB at 100ms

## Slide 35
Summary
Objectives for collectives in reconfigurable networks:
⇒ algorithms need to follow constrains of reconfigurable networks
⇒ reduction of required communication phases
⇒ reusable reconfigurable links

## Slide 36
Summary
Objectives for collectives in reconfigurable networks:
⇒ algorithms need to follow constrains of reconfigurable networks
⇒ reduction of required communication phases
⇒ reusable reconfigurable links
Reconfigurations during collective operations become desirable when: ⇒ Networks increase in size
⇒ Message size increases
⇒ Reconfiguration delay decreases

## Slide 37
Summary
Objectives for collectives in reconfigurable networks:
⇒ algorithms need to follow constrains of reconfigurable networks
⇒ reduction of required communication phases
⇒ reusable reconfigurable links
Reconfigurations during collective operations become desirable when: ⇒ Networks increase in size
⇒ Message size increases
⇒ Reconfiguration delay decreases
Email: juerss@campus.tu-berlin.de
Thank you!